## Slide 2: Wireless Security Attacks and Defence

## Slide 3: Agenda

## Slide 4: Agenda
10.00 - 10.30 Registration
10.30 - 12.30 Hacking 802.11
12.30 - 14.00 lunch
14.00 - 16.15 Securing 802.11

## Slide 5: Housekeeping
Fire + Flood
Other emergencies – the washrooms
Agenda

## Slide 6: Who am I – Who ate all the pies?
First UK Internet banks
WapGap
WIDZ
Contrib CEH
Zer0 day vulnerabilities including 802.11
CISSP, CCNE, CLAS CSSP
Mark Osborne - loud-fat-bloke

## Slide 7: The business - The opportunity and the threat

## Slide 8: The Background – What is it and how does it work?

## Slide 9: Background
What is it?
Types of WiFi
How it works?
The opportunity
How it could enhance our lives
The threat
Is there a threat?
Impact

## Slide 10: Types of Wifi
802.11b - Most common standard 2.4 Ghz + Wep
802.11a - Some license restrictions
  54 Mbps, 5GHz – Higher performance
802.11g - Higher speed
  2.4 GHz band (20-54 Mbps)
802.11i - Much better security
  Implementation of 802.1x and TKIP
  Secure de-authentication
  Secure disassociation, and
  Enhanced encryption with AES-CCMP
WPA + WPA2

## Slide 11: Network Type Adhoc V’s Infrastructure
Adhoc Network
Peer-to-peer
Seldom used commercially

## Slide 12: Types of 802.11 network Adhoc V’s Infrastructure
Access Point
The key to wireless security - controls the setting for the whole of the wireless network
Think of it as a hub (not a switch) on the network
Server farm
Corporate
WIRED
Network
Corporate
WIRELESS
Network
Infrastructure Network
Client
BSSID location software
Card
Normal
LAN

## Slide 13: Business Opportunity

## Slide 14: Business Opportunity
Wireless versus Wired cost
Estimates vary but all surveys suggest wireless is cheaper by up to 50% (hype)
Mobility and Connectivity
Browsing in Starbucks (Yawn) – What about hot spots in Airports and Hotels?
Interactive Seminars
New applications
Mobile bar-code scanners – Wireless credit card terminals
Dispatch lists printed in the drivers cabs
With no bespoke hardware

## Slide 15: Threats and Risks

## Slide 17: Objectives- Is there really a problem?
The London Wireless Hacker survey set up a number of dummy wireless networks around London to see who hacked into it.
Based on the rhetoric and hype, I defined 3 broad categories of activity. We then built an advanced Honeypot and deployed it in three separate London locations.
It detected:
War-driver - someone who probes the network but makes no attempt to access any resources
“Free surfer” - someone who connects to the network and attempts to surf the Internet
Wireless-hacker - someone who connects to the network and attempts to access or disrupt systems

## Slide 18: Is there really a problem? Survey Results

## Slide 19: The Results - malevolent attacks
From SNORT
  SNMP
  WEB-IIS ISAPI .idq +.ida access
  WEB-MISC http directory traversal + /etc/passwd
  Translate f
  Xping
  A nonsense DOS attack
From web-log
  Get OPTIONS
  GET /index.jsp
  Logins to Administrator/admin/root/guest/test

## Slide 20: Is there really a problems
So wireless hackers DO exist!!!
But what harm do free-surfers do?
  Data protection act
  Other regulation (FSA etc)
  Bandwidth and service-levels
  What if a free surfers hacks another org. from your internet or downloads porn?
  OR if a free surfers gets a virus from you
  OR gives you a virus or uploads porn

## Slide 21: Where?

## Slide 22: Insecure networks

## Slide 23: Why do we give so much air-time to the uninformed?
Are You
Really
NICE!!
After the survey, the BBC did a piece on it. This blokes argument was the firm that conducted was evil AND that
Wireless Aps were secure, people could only connect to them because the owners wanted to share bandwidth
That nobody would abuse such Niceness

## Slide 24
But oh look people are abusing it
And going
To prison for doing so!!!!

## Slide 25: The 802.11 tools and the attacks

## Slide 26: The 802.11 tools and the attacks
Network discovery - Finding out which wireless networks exist
  Kismet
  NetStumbler
  Wellenreiter.
Looking at traffic - Sniffing an 802.11 network
Cracking WEP Encryption keys
  Airsnort
  WEPcrack
I didn't break it - DoS
  Mark’s video sender
  Void11
  FakeAp
  WlanJack & FataJack
Getting in - Man in the middle attacks
  Monkey_Jack
  AirSnarf
  Hotspotter

## Slide 27
State 4
Registered
State 2
Authenticated
But not Associated
State 3
Associated +
Authenticated
State 1
Not
Associated
Linking with an AP
PC software detects beacons
Authenticate – open system or
encrypted
Associate
Create layer 2 sess

## Slide 28: 802.11 Frame Layout

## Slide 29: Beacon Frames
Sniffed frame (only 802.11 header)
  FC=0x0080 mgmt::beacon pver=0
  dur=0 frag#=0 seq#=1221
  DA=ff:ff:ff:ff:ff:ff SA=00:30:ab:1b:9b:cc BSSID=00:30:ab:1b:9b:cc
  Beacon frame body:
  Timestamp: 0000016d64ba92
  Beacon interval: 100
  Capability information: 0x0021 ESS Short_Preample[802.11b]
  ElemID #0 (Service Set Identify (SSID)):
  len=8 576972656c657373 = Wireless
  ElemID #1 (Supported rates):
  len=4 82848b96 = (Mbit/s) BSSBasicRateSet: 1 2 5.5 11 Others:
  ElemID #3 (DS Parameter Set):
  len=1 06 = Current_Channel=6
  ElemID #5 (TIM):
  len=4 01020000 = DTIM_Count=1 DTIM_Period=2 Bitmap_Control=0x00 Partial Virtual Bitmap: 00

## Slide 30: Probe Request Frame
Opening raw packet socket for ifindex 4
  Sniffed frame (only 802.11 header)
  FC=0x0040 mgmt::probe_request pver=0
  dur=0 frag#=0 seq#=1677
  DA=ff:ff:ff:ff:ff:ff SA=00:90:4b:06:3d:74 BSSID=ff:ff:ff:ff:ff:ff
  Probe request frame body:
  ElemID #0 (Service Set Identify (SSID)):
  len=8 576972656c657373 = Wireless
  ElemID #1 (Supported rates):
  len=4 82840b16 = (Mbit/s) BSSBasicRateSet: 1 2 Others: 5.5 11
Then
  Sniffed frame (only 802.11 header)
  FC=0x0040 mgmt::probe_request pver=0
  dur=0 frag#=0 seq#=1678
And then
  FC=0x0040 mgmt::probe_request pver=0
  dur=0 frag#=0 seq#=1681

## Slide 31: Probe_Response Frames
Sniffed frame (only 802.11 header)
  FC=0x0050 mgmt::probe_response pver=0
  dur=664 frag#=0 seq#=1273
  DA=00:90:4b:06:3d:74 SA=00:30:ab:1b:9b:cc BSSID=00:30:ab:1b:9b:cc
  Probe response frame body:
  Timestamp: 0000010d6b624c
  Beacon interval: 100
  Capability information: 0x0021 ESS Short_Preample[802.11b]
  ElemID #0 (Service Set Identify (SSID)):
  len=8 576972656c657373 = Wireless
  ElemID #1 (Supported rates):
  len=4 82848b96 = (Mbit/s) BSSBasicRateSet: 1 2 5.5 11 Others:
  ElemID #3 (DS Parameter Set):
  len=1 06 = Current_Channel=6
Sniffed frame (only 802.11 header)
  FC=0x00d4 ctrl::acknowledgement pver=0
  dur=350
  RA=00:30:ab:1b:9b:cc
  data: 06 09 04 00 02 01 12 01 02 01 00 00 00 00 00 00 00 00 00 00 00 00 00
  00 03 00 bc 45 03 01 06 05 04 01 02 00 00

## Slide 32: Authentication
Sniffed frame (only 802.11 header)
  FC=0x00b0 mgmt::authentication pver=0
  dur=218 frag#=0 seq#=3002
  DA=00:90:4b:06:3d:74 SA=00:30:ab:1b:9b:cc BSSID=00:30:ab:1b:9b:cc
  Authentication frame body:
  00 00 02 00 00 00
  Authentication Algorithm Number: 0=Open System
  Authentication Transaction Number: 2
  Status code: 0=Successful
Sniffed frame (only 802.11 header)
  FC=0x00d4 ctrl::acknowledgement pver=0
  dur=0
  RA=00:30:ab:1b:9b:cc
  data: 06 09 04 00 e8 00 2f 01 e7 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 03 00 9c 45 03 01 06 05 04 01 02 00 00

## Slide 33: Association Request
Sniffed frame (only 802.11 header)
  FC=0x0000 mgmt::association_request pver=0 dur=258 frag#=0 seq#=1911
  DA=00:30:ab:1b:9b:cc SA=00:90:4b:06:3d:74 BSSID=00:30:ab:1b:9b:cc
  Association request frame body:
  Capability information: 0x0001 ESS Listen interval: 1
  ElemID #0 (Service Set Identify (SSID)):
  len=8 576972656c657373 = Wireless
  ElemID #1 (Supported rates):
  len=4 82840b16 = (Mbit/s) BSSBasicRateSet: 1 2 Others: 5.5 11
Sniffed frame (only 802.11 header)
  FC=0x0010 mgmt::association_response pver=0
  dur=218 frag#=0 seq#=3003
  DA=00:90:4b:06:3d:74 SA=00:30:ab:1b:9b:cc BSSID=00:30:ab:1b:9b:cc
  Association response frame body:
  Capability information: 0x0021 ESS Short_Preample[802.11b]
  Status code: 0=Successful
  Association ID (AID): 49272
  ElemID #1 (Supported rates):
  len=4 82848b96 = (Mbit/s) BSSBasicRateSet: 1 2 5.5 11 Others:

## Slide 34: 802.11 tools - discovery
Active
  netstumbler
  ApSniff
  GTKSKAN
  Wardrive
Passive
  Kismet
  Ethereal
  Wellenreiter

## Slide 35: Discovering Wireless Access Points: NetStumbler

## Slide 36: Discovery – A war driving example
Response
SSID=Bert
Probe
Response SSID=fred
Probe
AP = Bert
AP = Fred
007f77ff7 Fred
0cac76ad1 Bert

## Slide 37: 802.11 tools - discovery
Passive
  Kismet
  Wellenreiter
Detection
No turnkey detection method at the moment for cards in monitor mode
Possible drop in signal drop in signal quality /noisy
Or response to broadcast packets

## Slide 38: Discovering Wireless Access Points: Kismet

## Slide 39: Discovering Wireless Access Points: Wellenreiter - Demo

## Slide 41: They’ve discovered the network
How do they attack it

## Slide 42
Server farm
Corporate
WIRED
Network
Target 2 - the client pc makes an ideal target
Target 1 - The traditional target, using the wireless network to get in the corporate network
Unauthorised
Access point
Target 3 - the Access Point and the wireless network
Attack points
UNWIRED
Network
Target 5 - Access points or Monkey-jack steal sessions in a man-in-the-middle attack
Target 4 - use rogue access points or laptops with WifI enabled to gain access to core networks

## Slide 43: Target 1- breaking in via the AP

## Slide 44: Target 1- breaking in via the AP
If you use no access control, they are in straight away – all they do is associate
If you use MAC authentication they will sniff it
  See next session
If you use 128b static WEP it is a question of time and traffic
  Everybody has heard of how easy it is to hack a WEP
If they can’t get in they will dos you
  Using void or wlan_jack or Fata_jack (target 3)

## Slide 45: Sniffing Wireless

## Slide 46: Sniffing 802.11 and Cracking Wep
Wired Equivalent Privacy (WEP) uses the RC4 encryption algorithm - Symmetric-key stream cipher
WEP (as defined in the standard) uses 64-bit shared keys
  Initialisation Vector (IV) is 24 bits of the key and sent as plain
  40 bit key
WEP provides no forgery protection & no replay protection (crc)
WEP misuses the RC4 encryption algorithm
  Static portion of IP packet allows known text attack
  IV wraps around, data can be easily recovered
Lack of automated key management

## Slide 47: Cracking Wep
WeakIVGen.pl Specify a key, and the program will generate a file "IVFile.log" that contains IVs that weaken each character of the secret key entered. The format for entering the key is "00:01:02:03:04" where each digit is a decimal value of actual key character, and the ":" character is used to delimit each key character.
prism-getIV.pl This script reads prismdump/Ethereal capture files, and looks for weak IVs in WEP traffic. If weak IVs are found, they are placed in the file "IVFile.log" along with the 1st encrypted output byte. This script accepts input from STDIN or from a file specified on the command line. You can either run "prismdump | prism-getIV.pl" or run "prismdump > capturefile" and then "prism-getIV.pl capturefile"
WEPCrack.pl This script reads IVFile.log, and uses the weak IVs + encrypted output to determine the secret key used. It sometimes guesses wrong, so additional logic will be added soon to do some additional checks.

## Slide 48: Airsnort
Airsnort is tool which cracks encryption keys on 802.11b WEP networks.
AirSnort operates by passively monitoring transmissions, computing the encryption key when enough packets have been gathered.

## Slide 49: 802.11 Hacker tools – wep cracking
DEMO

## Slide 50: Target 2 – the pc client

## Slide 51
(Mootar) morons. (Mootar) these people who live in my apartment complex are connected to my wireless (Mootar) they must think they're super-cool hackers by breaking into my completely unsecure network
(Mootar) unfortunately, the connection works both ways (Mootar) long story short, they now have loads of porn on their computer
IP Network traffic is Bi-directional

## Slide 52: Access to lap-tops (target 2)
When you connect to an open hot spot your PC is connected to a live network
If you have open shares
Or remote assistant open this will be a target
If “ad hoc” mode is not disabled
You disserve what you get

## Slide 53: Target 3 – attacking the access point

## Slide 54: Examples of Access point attacks
Basic infrastructure hacking
Is administration disabled over the wireless interface
How is administration controlled
  Over web
  Over telnet
  Over SNMP
Has the default passwords or community strings been changed

## Slide 55
Screen from the NetGear manager
Passwords (& SNMP community string ) unset
The default is Public and Private

## Slide 56: FakeAp –a confussion attack

## Slide 57: 802.11 Hacker tools - Fake-AP
Server farm
Corporate
WIRED
Network
AP = Bert7
AP = Bert2
AP = Bert6
AP = Bert3
AP = Bert4
AP = Bert1
AP = Bert5
AP = Bert8
AP = Bert11
AP = Bert17
Which
Bert!!!!

## Slide 58: 802.11 Hacker tools - Fake-AP
Sends beacon packets with spoofed Mac and dummy SSID to simulate multiple APs. This confuses most client Wireless network card software and war-driving code.
  More interesting as an active defence against hackers
 Hundreds of SSIDS appearing
 No certain vaccination

## Slide 59: Fakeap
Detection
packet_number:2 frame-control-type:Management(0) subtype: Beacon (8)
packet-time:1050313458:349282 mac-address-1:0xffffffffffff mac-address-2:0x00800f8386a0 mac-address-3:0x00800f8386a0
SSID:pepo41
packet_number:13 frame_control:type:Management(0) subtype: Beacon (8) packet_time:1050313459:29783 mac-address-1:0xffffffffffff mac-address-2:0x0008c742bfc0 mac-address-3:0x0008c742bfc0
SSID: gretel
packet_number:72 frame_control:type:Management(0) subtype: Beacon (8) packet_time:1050313462:89870 mac-address-1:0xffffffffffff mac-address-2:0x00800f06914e mac-address-3:0x00800f06914e
SSID:contend

## Slide 60: 802.11 Hacker tools - Fake-AP
DEMO

## Slide 61
Wlan_jack & Void DOS ATTACKS
1. Corporate security team happily monitoring the internet for porno
Deassociate
2. Hacker PC sends disassociate to tear down session
.
Deassociate
Deassociate

## Slide 62: 802.11 tools - Hacks
Void11
- sends Authentication packets
- sends Association packets
  Look for a random mac address
  A massive increase in Frames (layer2) with no increase of IP PACKETS (layer 3)
   No certain vaccination

## Slide 63
Linsucks # void11_hopper &
Linsucks # void11_penetration -D wlan1 -S pants -m 40

## Slide 64: 802.11 tools - Hacks
Aero-jack: Airjack driver allows MAC address to be set and raw packets to written. Package includes:
    ESSID-jack
    WLAN-jack
    Monkey-jack
Then
    FATA-jack was added
Aero-jack was revolutionary but now the hostap driver has the same capability

## Slide 65: 802.11 tools - Hacks (2)
wlan-jack - Wlan-jack sends deauthentication packets at a high rate of 5 every second to the AP tearing down a session
  As the malevolent packets are spoofed, usually high-values, MAC protection will not prevent it
  As the malevolent packets are mgt packets, WEP protection will not prevent it (mgt packets are not encrypted)
  Look for the MONKEY JACK BSSSID
  A massive increase in Frames (layer2) with no increase of IP PACKETS (layer 3)
   No certain vaccination

## Slide 66: WLAN-jack
Detection
packet_number:456
frame_control:type:Management(0)
subtype: Deauthentication (12)
    mac-address-1:0xffffffffffff
  mac-address-2:0x0030ab1b9bcc
  mac-address-3:0x0030ab1b9bcc
  sequence:40208 (0x109d)
packet_number:457
frame-control-type:Management(0) subtype: Deauthentication (12)
mac-address-1:0xffffffffffff mac-address-2:0x0030ab1b9bcc
mac-address-3:0x0030ab1b9bcc sequence:40224 (0x209d)
 Look for subsequent out-off step data packets from client
Plus large volumes of traffic

## Slide 67: Fata_Jack – a cleint ddos

## Slide 68: Fata_Jack
FATA-jack – This attack got some bad press, almost entirely from one US Unix SysAdmin website – took a comment by me in the first line of the code “that I ripped-off” some literal definition – Then called it a Rip of Monkey-Jack (actually the line were from WLAN-JACk). Never mind their website shows that they struggle to FSCK a filesystem
Moving on (not giving air time to the uniformed)
This attack is included in most US computer security University course – one actually features it as a term project “to try and figure out how it works”

## Slide 69: Fata_Jack
FATA-jack
Although there is no doubt that the author isn’t as clever as the designers of Void or WlanJack, the attack was designed to be a defence.
It was going to be included as a SHUN function in the WIDZ ID. Because it does damage:
the AP
Or use floods and use much bandwidth
But does cause most WIFI PCs to need to be rebooted and drivers reloaded

## Slide 70: 802.11 tools - Hacks (2)
FATA-jack by ME - a modified version of the Wlan-jack,
Fata-jack sends Authentication packets with an invalid algorithm to the AP tearing down a session.
In many cases causing the client driver or client software to fail with a buffer overflow, requiring a reboot
  As the Malevolent packets are spoofed, MAC protection or WEP protection will not prevent it
  Not a flood attack – rates as low as at a rate of 1 every 25 seconds can cause clients to die
  algorithm = type 2
  a sequence number and status code both set to0xffff.
   No certain vaccination

## Slide 71: Fatajack
Detection
PC --> Ap
packet_no:141 frametype:Mgmt(0) subtype: Auth(11) mac1:0x0030ab1b9bcc mac2:0x00904b063d74 mac3:0x00904b063d74 AlgNo:(0x0200) Unknown TransNo: 0xffff Status_code: 0xffff
packet_no:142 frame_type:Control(1) subtype: ACK (13) mac1:0x00904b063d74 mac2:0xffffffff0000
Ap --> PC
packet_no:143 frame_type:Mgmt(0) subtype: Auth (11) mac1:0x00904b063d74 mac2:0x0030ab1b9bcc mac3:0x0030ab1b9bcc mac4:0x020000000d00
AlgNo:(0x0200) Unknown TransNo: 0x0000 Status_code:( 0x0d00) 13
packet_no:144 frame_control:type:Control(1) subtype: ACK (13) mac1:0x0030ab1b9bcc mac2:0xffffffff0000

## Slide 72: Target 4 – Rogue AP or Evil Twin
Rogue Ap – some idiot from marketing plugs in a badly configured AP on the corporate lan and then you get hacked
Doh!!!

## Slide 73: Target 4 – Rogue AP or Evil Twin
Evil Twin – old hack, new name
some one sniffing the airways near your office discovers that you have loads of PC’s that want to associate with a random set of SSIDS
He continues Sniffing but sets up an AP to see if any of these laptops will automatically associate with him
If one does, he sets up the DHCP on the AP to allocate an IP and a route. Then from another station on that bogus network starts NMAPing u
Exactly like auto-answer modems on boxes

## Slide 74: Target 5 – Man in the middle
Monkey_jack
AirSnarf
Hotspotter

## Slide 75: MITM – Hardware attack
Can be done
Like Evil-twin with a linux box and an AP

## Slide 76: 802.11 tools – Target 5 man in the middle
Monkey-jack
    As classic Man-In-theMiddle attack
      1 WLAN JACK to deasso session from
      2 ESSID-Jack to retrieve AP(s) essid/mac
      3 set your interface to the above
      4 steal session when it re-associates
Before
After

## Slide 77
Monkey jack – the ultimate hack
1. Corporate security team happily monitoring the internet for porno
ESSID = Wireless
Channel =6
Deassociate
2. Hacker PC sends disassociate to tear down session
3. Hacker PC sends Beacon pretending to be AP “Wireless” on channel 9
.
Beacon chan 9 Wireless
4. Corporate security team establish session with
ESSID = Wireless
Channel =6
5. All old traffic plus some exciting new stuff routed through
Hacker PC

## Slide 78: Monkey-jack Detection
Look for WLAN-jack + a new AP with MAC same as yours on a different channel
My real AP beaconing
FC=0x0080 mgmt::beacon pver=0
  DA=ff:ff:ff:ff:ff:ff
  SA=00:30:ab:1b:9b:cc
  BSSID=00:30:ab:1b:9b:cc
  Capability information: 0x0021 ESS Short_Preample[802.11b]
  ElemID #0 (Service Set Identify (SSID)):
  len=8 576972656c657373 = Wireless
  ElemID #1 (Supported rates):
  len=4 82848b96 = (Mbit/s) BSSBasicRateSet: 1 2 5.5 11 Others:
  ElemID #3 (DS Parameter Set):
  len=1 06 = Current_Channel=6
The bogus AP attempting to hijack connections
FC=0x0080 mgmt::beacon pver=0
  DA=ff:ff:ff:ff:ff:ff
  SA=00:30:ab:1b:9b:cc
  BSSID=00:30:ab:1b:9b:cc
  Capability information: 0x0021 ESS Short_Preample[802.11b]
  ElemID #0 (Service Set Identify (SSID)):
  len=8 576972656c657373 = Wireless
  ElemID #1 (Supported rates):
  len=4 82848b96 = (Mbit/s) BSSBasicRateSet: 1 2 5.5 11 Others:
  ElemID #3 (DS Parameter Set):
  len=1 09 = Current_Channel=9

## Slide 79: Kracker-Jack
Kracker-jack (KJ) is a proof of concept attack which subverts a freeware IPSEC VPN used in wireless deployment.
Although the concept will not transpose to all IPSEC VPN implementations – it could be modified for some
  inserts to 802.11 layer (like monkey-jack)
  KJ gets victims public key from DNS server
  KJ, using the victims MAC address sends DHCP request with its own key to replace the victim’s key in the DNS server

## Slide 80: Kracker-Jack
  KJ initiates ISAKMP main mode SA with the target server
  KJ initiates ISAKMP main mode SA with victim
  Victim gets new server key by DNS request serviced by KJ
  Two separate IPSEC tunnels are now setup
  All traffic passes through KJ unencrypted

## Slide 81: 802.11 Hacker tools – MITM attacks
DEMO
Monkey_jack
AirSnarf
Hotspotter

## Slide 82: 802.11 tools - Hacks
THCRUT
- ping
- rarp
- DHCP

## Slide 83: 802.11 Hacker tools
DEMO

## Slide 84: Wireless Security Attacks and Defence